Title
L1Calo DBs: Status and Plans
Murrough Landon
20 November 2006
Overview of L1Calo databases
Present status
Plans

---
L1Calo Database Overview

---
Overview of Status and Plans
Present status
  - At present much L1Calo information used online is in the OKS configuration database: HW configuration, cabling, calibration, trigger menu, run types, etc.
  - Exception: Preprocessor configuration & calibration in XML
  - Also some “flat” data files used by a few applications
Intentions
  - Trigger menu will move to new CORAL based configuration
  - Calibration data should move to COOL
    - Also Preprocessor configuration (integrated with calibration data)
  - Consider moving other L1Calo configuration data from OKS
    - Or are new OKS configuration archiving tools enough?
  - Description of connectivity? (See later)

---
Constraints
Not just USA15
  - Production test and maintenance sites use TDAQ software
    - Test/diagnosis of single module needs multiple crates
  - Want common software and database everywhere
    - Eg Oracle at CERN, SQLite/MySQL elsewhere
  - Tools need to work on small scale, not just ATLAS scale
    - Eg hand edited configurations as well as TC database extracts
  - Ideally minimise different sets of SW packages needed
    - Trigger configuration DB recently moved to “ATHENA” style DetCommon package needing separate installation :-(

---
Calibration Procedures
Digital timing
  - Standalone online runs, scan clock phases and delays, read parity errors from VME, store results (incl. Histograms)
Analogue timing
  - Constant calibration pulses from calorimeters (joint runs), scan clock phases, process event data, store results
Pulse shapes
  - As above, may want to look at several energies
(Electronic) energy calibration
  - Calibration pulses at ranges of energies, process event data (also calorimeter readout), store results
NB L1Calo calibration data is only used online
  - Although some processing may be offline (Athena)

---
Calibration Database
General proposal
  - Use pure COOL for now (think about CORAL later)
  - Results for all calibration runs stored in one set of folders
  - Separate validation procedures copy data to another set of folders which are used to configure the system
  - Separate folder for each type of component to be loaded
    - Eg different types of module, submodules, channels
  - When storing calibration data, separate folders for each type of calibration procedure
    - Validation procedure may combine results of separate calibrations for components of the same type
  - Channel IDs coded with crate, module, submodule, channel
    - HW identifier best for online to quickly select data from one crate
    - But might not be so natural for Athena based calibration SW?

---
Connectivity
Present L1Calo status
  - Digital cabling presently described in OKS
    - Private L1Calo schema – something similar to be in tdaq-01-07
  - Started description of analogue cabling including pin to pin patch panel interconnections in relational DB
    - Source is Excel spreadsheets used in cabling documentation
    - Not yet complete, nor yet used in online or offline code
Issues with TC database
  - Common approach assumes TC databases as master from which data is extracted into more useful databases
  - Problem with limited access for updates
    - Friday afternoon recabling to work around a problem?
  - Full description, including patch panels, need extracts from both Cabling and MTF/Rack Wizard?

---
Other Recent Activity
Configuration DB archiving
  - Recently tried using oks2coral & oks2cool
  - For remote test sites want to use SQLite and/or MySQL
  - Some problems
    - SQL scripts to initialise oks2coral DB needed fixing for SQLite
    - TDAQ release doesnt fully support SQLite

---
Plans
Calibration Database
  - Imminent “experts week” to make (long delayed) progress on getting calibration procedures working with COOL
    - Current COOL based prototype still lacks the Run Control link
  - Need to update all calibration procedures
  - Further work on tools, trends, validation etc
Configuration
  - Look at PartitionMaker for generating L1Calo segments
    - But from what master source?
  - Aim to move “operational choices” from OKS?
Connectivity
  - Generate digital cabling for new OKS schema
  - Need to consider strategy for analogue cabling DB