Title
M5 Summary
Murrough Landon
27 November 2007
(with special thanks to Norman's run reports)
L1Calo Setup
Aims
Reality
Operation
Problems
Summary

---
L1Calo Setup in M5
Preprocessor Barrel (4 crates)
  - Three endcap crates available, but not read out
Nearly complete CP system (but only barrel read out)
  - Only one CMM per crate (“tau” thresholds)
Complete JEP system (but only barrel read out)
Roughly half the final readout (11/20 RODs)
  - Three links to RoIB
Non-standard arrangement of readout
  - Some ROD source IDs wrong
    - Need special fixup in bytestream decoders

---
L1Calo Setup in M5

---
Aims
Tune preprocessor for a good cosmic trigger
  - DAC scan, pedestal at 40 ADC counts
  - Simple lookup table (straight line, with pedestal subtraction)
  - Use LUT to zero any problem channels
  - Adjust tower to tower timing using Tile laser calibration
    - Also add top/bottom correction for cosmic timing
  - If possible, do the same with LAr pulser
Prepare suitable trigger menu
  - Tau and jet triggers at various thresholds
Time in trigger through the system to the CTP
  - Using Tile laser pulses
Trigger ATLAS from L1Calo
  - First with laser, then see if we can trigger on cosmics

---
Week 1: Integration Tests
Friday afternoon before M5 (after L1Calo meeting)
  - Hasty move to tdaq-01-08-03, just in time for weekend run
Weekend before M5
  - Smooth cosmic data taking with calorimeters
First week reserved for integration tests
  - L1Calo integration on Monday afternoon
    - Test run states, high rates with ECRs - OK
      - L1Calo limited to 25kHz with 5 slices in neutral mode
  - Joint LAr+Tile+L1Calo integration tests Wednesday pm
  - Rest of the week free for last minute work!
Weekend run
  - Pixels, LAr, Tile, L1Calo, MDT, RPC, TGC, HLT

---
Week 1: Standalone
New PPr DAC scan
  - Applied limits to DAC slope and offset
    - Set “success” flag to false if outside limits
    - Failing channels have their LUT zeroed
    - MCMs 12&13 disabled in SW (DAC setting problem area)
Tried to set CMM timing
  - Crate timing OK, but couldnt set time to capture remote cable data in System CMM
    - SW feature fixed after M5 (but still have this problem in CP?)

---
Week 2: Integration
Monday: integrated high rate test (all detectors)
  - Reached 50kHz with L1Calo included
    - RODs in native mode with zero suppression and some PPMs disabled
      - L1Calo was about 2% BUSY – but then one ROD stuck BUSY after 20 minutes

---
Week 2: L1Calo Trigger (1)
Tuesday: dedicated to L1Calo
  - Checked CMM-CTP connection with ramps: all OK
  - Tried to time in four CMM-CTP cables (tau,2*jet,energy)
    - All OK, but our different cables have widely differing phases
    - CTP cannot easily handle this, so we only used the main jet triggers
  - Tile laser activated with TileCal cosmic trigger
    - Found L1Calo jet triggers in CTP
      - Timing scattered, so disabled all except one JEM
    - With PPr tower timing adjusted for the barrel, L1Calo trigger was two ticks ahead of (much delayed) TileCal cosmic trigger
      - With additional PPr delay to cope with endcaps, we will be later...
      - But for M5 we added an extra two ticks delay at the CTP
  - L1Calo trigger enabled (and TileCal trigger disabled)
    - Triggered ATLAS (actually just TileCal) with L1Calo trigger
    - Check that TileCal see their pulses at the same time
    - Success!

---
Week 2: L1Calo Trigger (2)
Wednesday: also dedicated to L1Calo
  - Tried to equalise PPr tower timings with TileCal laser run
    - Failed to see pulses in large areas of the TileCal
    - Eventually gave up
      - System handed over to LAr and RPC to investigate their own problems
      - In return we got more dedicated L1Calo time on Thursday
  - But level 2 reported that yesterdays RoIs make sense
Thursday: retry Wednesday
  - Really no TileCal signals seen on the cables with a scope
    - Abandoned our dedicated time
    - Later Monica diagnosed a TileCal TTC problem
      - Understood but needs power cycle to recover TTCrx for adder boards
Weekend
  - Standard cosmic run (with L1Calo trigger)

---
Operation
DCS
  - Worked very smoothly
Online Monitoring (AthenaPT and GNAM)
  - Very useful plots from all monitoring programs
    - Especially when hunting for problems
Offline Tools
  - Analysis of CBNT also very helpful
    - See talk by Damien earlier today
Shift crew
  - More to look at, but apologies that experts were still running around, either too busy to explain what was going on or in complete ignorance themselves
    - We need to sort out shifter duties, training and documentation

---
AthenaPT Monitoring (1)

---
AthenaPT Monitoring (2)

---
Offline Analysis

---
Problems
ROD BUSY
  - One ROD stuck in BUSY state two or three times
    - Much better than M4 but still needs fixing
    - NB many other detectors also had BUSY problems
Monitoring
  - Problem of monitoring programs dying
    - Later diagnosed as a TDAQ bug, now fixed
  - AthenaPT: slow to start and fails reconfigure
    - Try to analyse LAr+Tile+L1Calo
    - Initialisation will move to first event in the future
DAC scan issues
  - Still have problem with first point in the scan
  - Some channels have poorly measured slope
    - Now understood – need more points in the scan

---
Summary
We did provide a trigger to ATLAS
  - And have done better in subsequent cosmic runs
We do have some useful monitoring and analysis tools
  - But always room for improvement...
But we still have:
  - many problems to fix
  - many tools to improve
  - many tools to implement!
Thanks to all who took part