Title
L1Calo Databases
Murrough Landon
16 June 2008
Overview
Trigger Configuration DB
L1Calo OKS Database
L1Calo COOL Database
ACE

---
L1Calo Database Overview

---
Trigger Configuration Database
Contents
  - complete description of Level 1 and HLT trigger menus
  - includes separate prescales and other CTP settings
  - developed by trigger configuration group
L1Calo
  - until last week we were still using a private OKS based trigger menu that only contained L1Calo specific settings
    - satisfactory and stable for over six years
  - now (finally!) linked to trigger configuration database
    - requires DetCommon: dependency on tdaq and offline SW
  - first successful load of L1Calo hardware from oracle DB last friday

---
L1Calo OKS Database
Contents
  - usual description of segments, hardware and applications
    - most of our hardware objects are now also Resources
  - also description of internal digital cables
    - mainly via Cable objects (historical)
    - also added Resources and ResourceSets to link with ROS and to provide more granularity in disabling parts of the trigger hardware
  - definition of data sources/sinks for internal tests
  - private (L1Calo only) trigger menus
    - soon to be discontinued
Source
  - hardware segments and cabling now generated by script
    - internal cabling is algorithmic, no connection to TC database yet

---
L1Calo COOL Database
Contents
  - results of all calibration runs
    - historical record for trends
    - even if never used to configure the system
  - sets of “validated” calibrations
    - subset of calibration results that pass validation checks and are significantly different from previous validated calibration
  - run parameters
    - global settings for configuring both Physics and calibration runs
  - configuration parameters
    - operation settings, at module or channel level

---
Calibration and Database Procedures
Operational model
  - configure calibration run from COOL
  - take calibration data
  - store calibration results
  - run validation procedure
    - update validated calibration results if appropriate
  - normal runs use latest validated calibration data

---
Implementation Status (1)
General
  - Basic scheme in operation for over a year
  - Reasonably happy with it
Improvements Required
  - Need better handling of error codes when validating Preprocessor calibrations (results of several different types of calibration get combined)
  - Consistent use of error codes across the L1Calo system
  - Need to track module IDs for the whole system
    - Only done for purely online procedures at the moment
  - Further schema changes need for some preprocessor data

---
Implementation Status (2)
Preprocessor
  - analogue pulse pedestal measurement and setting
    - procedure presently running offline (could be online in GNAM)
    - works well, though further tuning of the algorithms desirable
  - coarse timing (BC level)
    - online timing scans OK within one calorimeter partition
    - not so easy to align different partitions (need beam!)
    - minor schema changes foreseen
  - pulse shape and fine timing
    - calibration procedures tested with pulsers but not really tuned
    - recently decided on schema changes
      - calculate filter coefficients offline rather than at time of use
    - pulse shape from calibration pulses not the same as from beam
  - energy calibration, Et correction
    - still under development...

---
Implementation Status (3)
Cluster & Jet/Energy Processor
  - digital timing at module and channel level
  - all modules obtain timing calibration from COOL
  - most calibrations now automated and writing to COOL
    - still manual for final merger modules (CMMs): very few channels

---
To Do List
Use Oracle!
  - Still using SQLite at point 1
    - Convenient while we are still making schema changes
    - Aim to switch to ATONR before beam...
Configuration data
  - Intend to move remaining configuration from OKS to COOL
Tools
  - Need more work on extracting, analysing and presenting trends in calibration results

---
ACE: A Cool Editor (1)
Features
  - COOL database browser and “editor”
    - Uses pure COOL API
    - Supports all LCG DB technologies including SQLite
  - Open multiple databases and folders
    - Select all IOVs or (by default) just the latest IOV [new]
  - Filters for selecting subset of channels [new]
  - “Edit” rows
    - clone existing row
    - modify values
    - commit updated row (gets new interval of validity)

---
ACE: A Cool Editor (2)
Availability
  - ACE is now packaged with the LCG COOL release
    - Latest bug fixes in COOL_2_5_0 (not in ATHENA 14.2.0)
  - Needs Qt 4 and LCG packages
    - Source various LCG setup scripts
    - Or run via L1Calo script at /afs/cern.ch/atlas/project/tdaq/level1/calo/bin/ace.sh
      - runs private copy of latest version
Restrictions
  - Only supports single version folders at the moment
Support
  - Web page coming soon...
  - Bug reports and feature requests to the author:
    - Chun Lik (Alvin) Tan: clat@hep.ph.bham.ac.uk

---
ACE Screenshot 1: Connect to New DB

---
ACE Screenshot 2: Connect to Known DB

---
ACE Screenshot 3: Browse Folders

---
ACE Screenshot 4: Filter Rows

---
ACE Screenshot 5: Clone Row to Edit

---
ACE Screenshot 6: Commit Modification