Title
DB and Information Flow Issues
Murrough Landon
28 April 2009
Selecting types of run
L1Calo databases
Archiving run parameters
Tools

---
Specifying Runs (1)
Different mechanisms evolved in each system
L1Calo
  - Different run types described by parameters in sets of COOL folders (one folder per run type)
  - A few additional parameters set only in IS
    - Mainly choices of which COOL folder and which group of OKS objects
LAr
  - Sets of XML or other data files with scan parameters
  - IGUI panels to update OKS database and publish to IS
  - LArShifter IGUI panel to control standalone runs
Tile
  - IGUI panels to update OKS database and publish to IS
  - Scan parameters described how?

---
Specifying Runs (2)
For combined L1Calo + LAr/Tile runs
  - Separate partitions for LAr, Tile and L1Calo master modes
    - Should be no need to change OKS configurations
      - Except enabling/disabling LAr/Tile in L1Calo master mode
  - Currently need to use L1Calo and separate Calo panels
    - OK for shifters (if we provide documentation)?
  - Might be nicer to develop something like LArShifter panel
    - But could we update all necessary calo information?
    - Whats the full list of everything that needs to be set?
Whats missing?
  - How to (easily) choose receiver gains via IGUI panel?
    - Would like this for L1Calo pedestal runs during LAr/Tile calibrations
    - Need to ensure safely back to Physics gains afterwards

---
L1Calo Calibration DB (1)
Existing COOL folders for
  - results of each calibration
  - validated calibrations
    - still missing sophisticated validation procedures
    - validation basically manual check of histograms
    - started work on comparison with previous calibrations
  - lists of dead/noisy channels
  - run parameters
  - global configuration
Additionally (but not yet used)
  - conditions for each run
    - set of towers disabled via resources
To be added
  - record of user choices for each run

---
L1Calo Calibration DB (2)
Still missing
  - Separate noise cuts for cosmics vs physics?
  - Trigger tower timing for cosmics
Untested
  - Pulse shape, energy scans, saturated BCID settings
To do
  - Use Oracle DB rather than private SQLite files
    - Would like to freeze all folder schemas first
    - Still not sure if some folders will change (run pars)
  - Receiver COOL DB
    - Is this still a private DB owned by chaouki?
    - If so, also move to production Oracle DB at some point?

---
L1Calo Calibration DB (3)
Database update procedures
  - DAC and pedestal runs can be analysed online
    - Though typically done offline with online SW
    - Can easily be updated to online databases
  - PHOS4 and energy scans analysed offline (CAF)
    - Need to transfer new results back to online DB
      - Both to L1Calo COOL database and DB for receivers
    - Not yet tried this

---
Storing Information about Calibrations
Tile:
  - CIS pattern structure stored with the event
  - Definition from C++/python
LAr:
  - XML files: archived somewhere?
  - Step in the sequence saved with the event (and parameters?)
L1Calo:
  - Sequence number saved in the event
  - Still need to store which type of run...

---
Tools
Missing
  - Better validation and stability tracking
  - Noise adjustment via rate metering