Title
L1Calo Phase 2 Upgrade
Murrough Landon
26 March 2009
Baseline Concept
Geometries
Granularity Options
Architecture and Fanout
Calo Issues
Summary

---
Introduction to L1Calo Phase 2 Work
Work done so far (a little)
  - Survey of ATCA, links and other technology
  - Survey of HLT algorithms we might steal
  - Thoughts on general L1Calo phase 2 architecture
  - Issues relating to mappings from FE and RODs
Work not done yet (lots more!)
  - Simulation, simulation, simulation
  - More simulation – especially of pile up
  - Detailed thinking about
    - Granularities
    - Algorithms
    - Architecture
    - Bandwidths
    - etc

---
Challenges of Phase 2 Upgrade
Huge increase in pileup
  - But no increase in basic detector granularity
L1 rate similar to the present one
  - But prefer not to increase thresholds for physics objects
Need better L1 algorithms
  - Borrow ideas from present L2?
Use finer granularity in eta, phi and depth at L1
  - New trigger tower (L1 primitive?) more than an Et sum
    - Lateral and/or depth profile and position information
    - Quality bits?
Not yet clear what granularity we need
  - For what efficiency, fake rate, threshold sharpness
Nor where or how to use it

---
Baseline Phase 2 Concept
Strong preference to digitise and transmit all cells every BC from the front end to off-detector pipelines
ROD/preprocessor:
  - generates Level 1 primitives (towers++) from calibrated Et for the correct BC
  - sends them to a separate L1Calo trigger processor
  - different LAr/Tile views of the ROD?
    - and still changing

---
Implications of On-Detector Digitisation
Allows much more sophistication in forming “towers”
  - New digital “L1 Primitive” could be a bit field with
    - Et (to greater precision than before if required)
    - Depth and lateral shower profile information, quality flags?
  - Better handling across boundaries?
  - Finer granularity (in EM layer)
    - Different granularities possible in EM and Hadronic layers
Single calibration for trigger and main readout
But brings trigger and readout closer together
  - Present architecture allows each branch complete freedom to optimise the organisation of their own system
  - Phase 2 upgrade will impose trigger constraints on layout of RODs and mapping of FE to ROD links
  - Also no (completely) independent readout path

---
Latency
Main upgrade scenarios:
  - No L1 track trigger: small latency increase possible to 3µs (constraint from muons?)
  - With L1 track trigger: need fast L0 seed from calo+muon (latency same as now, ie 2µs?)
  - Independent L1 track trigger (no L0 requirement): greatly increased latency, up to 6µs
Until any decision, assume that latency is still critical
No unnecessary deserialisation/reserialisation
  - Significant latency penalty (6 BCs?) at each such step
Unavoidable: FE->ROD, ROD->L1, L1->Merger/CTP(?)
Avoidable: everything else!
  - Eg between RODs, between L1 modules

---
EM Barrel Geometry
Each layer has a different geometry
  - Uniform in eta, except for barrel/endcap transition region
Middle and back compatible with 0.05*0.05 minitowers
But front (strips) and presampler (PS) cover 0.1 in phi

---
EM Endcap Geometries
Seven different layouts between eta=1.4 and eta=3.2
Many different ways cells are grouped into Front End Boards (FEBs)
NB two granularities in the EM barrel
One in the FCAL
(Plus similar in the hadronic layer)

---
Granularity Options (1)
Minitowers * depth samplings
  - Send 0.05*0.05 EM towers (0.025*0.05 PS,Front layers?)
    - Still 0.1*0.1 in hadronic layer (detector limit)
  - All depth samplings separate
    - Less need to organise cells in RODs
  - LAr data “reduction”: 60 cells -> 4+8+4+2 = 18 minitowers
    - Only factor 3 bandwidth reduction to L1Calo
      - But must then multiply by required phi fanout, up to factor 2?
    - 150 Tbits/s to LAr RODs: something like 50 to 100 Tbits/s to L1Calo
      - Plus 10% for hadronic layer
  - L1Calo expands to 8 crates in phi octant layout?
    - O(100) modules with O(0.5 to 1) Tbit/s per module
Alternative: minitowers summed in depth
  - Less bandwidth, but needs more cell organisation in RODs
  - How to match PS & Front layers to middle and back layers?

---
Granularity Options (2)
Semitowers?
  - Intermediate granularity: 0.05 in eta * 0.1 in phi
  - Add detailed lateral and depth profile information
  - Shower position within the semitower
  - Requires cells to be organised into towers in ROD FPGAs
  - Modest increase in present bandwidth to L1Calo
    - 25 bits/semitower => total O(10) Tbits/s

---
Granularity Options (3)
Supertowers, miniL1Calo
  - EM shower is well contained in existing 0.1*0.1 tower
  - Future LAr ROD FPGA might cover 0.2*0.2 with full depth?
    - 40 GBT links equivalent to two whole FEBs or 256 cells
    - Would need a lot of organisation of links into RODs
  - Run mini sliding window at full granularity in each ROD FPGA
    - L2 quality if shower is contained within one ROD FPGA
    - Option increasingly attractive as FPGAs & links get bigger & faster
  - Send found electrons or half electrons to L1Calo (at 0.1*0.1)
    - Another sliding window algorithm in L1Calo to fix up boundaries
  - Total bandwidth to L1Calo maybe 5-10 Tbits/s?
  - Might squeeze low granularity L1Calo into a single crate
    - No phi fanout required for single crate L1Calo
  - Issue: part of the L1 algorithm moves into LAr ROD domain
    - How to collaborate on development?

---
Present L1Calo Architecture
Separate EM/Tau and Jet/Energy processors
Sliding window algorithms
  - Requirement for environment
Phi quadrant layout
  - O(30%) fanout at source (PPM)
  - O(75%) fanout at CPMs/JEMs
  - Strong requirement on eta,phi shape covered by all modules
    - NB orthogonal to detector layout
Many remapping stages
  - Receivers (20 mapping variants), patch panels, PPMs

---
Possible Phase 2 Architectures (1)
Single processor module?
  - For all objects: EM,tau,jet
Still use sliding windows
  - Unless there is a better idea?
Fewer remapping stages?
  - May want fibre ribbon PPs?
Consider phi octant layout?
  - Similar fanout in L1 modules
    - Unless modules wider in eta?
  - O(75%) fanout from RODs
  - Fewer restrictions on eta,phi shape covered by RODs
    - But still need regularity

---
Possible Phase 2 Architectures (2)
Links from RODs duplicated to neighbouring octants
  - Either on ROD or intermediate fanout step?
Links to neighbouring L1 modules duplicated via crate backplane without reserialisation
  - Most efficient if links cover regular, squarish eta*phi areas

---
Downstream from L1Calo...
Topology and the CTP?
  - Phase 1 upgrade proposes additional L1Calo (plus muon) topological processor passing extra bits to the current CTP
What would be appropriate for phase 2?
  - Keep separate topological layer combining calo, muon and track trigger
  - Or combine topology with new CTP?
    - Another case of phase 2 boundaries possibly being different from now

---
Granularity: Links
ROD->L1 links
  - Sliding window algorithms require lots of fanout
  - For phi octant layout, this is most efficient if L1 link contains contains more “towers” in phi (2**n) but is narrower in eta
    - Not how the detector is organised (especially TileCal)
  - Small number of towers per link easier to handle
    - But greater number of serial streams to fanout
  - 1 Gbit/s is 25 bits at 40 MHz
    - Roughly one EM tower with Et and profile bits?
    - 6 Gbit/s would easily cover 4 towers (or mini-towers)
      - Likely possible to cover eta,phi space with 0.2*0.2 links
FE->ROD links
  - Group together cells onto links by towers if possible
    - Follow existing tower builder or Tile adder layouts?
      - Projective geometry in TileCal, not division by z?

---
Calorimeter Boundaries
Worst case (by far) is EM barrel/endcap transition
  - Anything we can possibly do will probably be needed
  - Sum cells across EMB/EMEC before making L1 primitives?
  - Add in crack scintillators? (Currently read out via Tile EB)
    - Upgrade being considered in that region
Cant do anything about crack at eta=0
Next worst is Tile LB/EB transition
  - Currently cells are deliberately misorganised to adjacent eta bins to avoid analogue summing across the boundary
  - Upgrade Tile ROD could handle it properly
  - Add in the gap/crack scintillators?
Least worst is Tile EB/HEC transition
  - Again, currently misorganised – could do better digitally

---
LAr Front End Board Layout
Diagram shows eta,phi sizes of FEBs in different regions
  - Sketched on 0.1*0.1 tower grid
Barrel, endcap & FCAL have many different geometries between (and within them)
Transition regions span boundaries in both eta & phi
Bring all layers to one ROD requires splitting some FEBs between two or four RODs
  - Is this a problem (in principle)?

---
Summary
(Much) more simulation and thought required to:
  - Identify optimal and workable algorithms
    - What can be implemented in firmware and in whose FPGA?
  - Derive viable L1Calo architecture in more detail
    - Whats in a tower? What extra information (apart from Et)?
    - What granularity do we need?
    - What bandwidth can we (and the RODs) handle?
  - Discard any unnecessary “worst case” scenarios
Need to discuss implications of FE and ROD layouts
  - What is desirable/acceptable/undesirable/unacceptable to the LAr and Tile groups?
  - Some options have significant impact on ROD organisation
  - Issues of boundaries of responsibility?

---
Backup Slides

---
Channel and Link Organisation (1)
Lessons from existing L1Calo
  - Worry about the difficult areas early in the design process
    - It only gets worse later (and dont forget about the FCAL!)
  - Do as much as possible at the first stage in the chain
    - Irreducible constraints from calo geometry will hit later
Link organisation
  - Data processed together needs to be brought the same chip!
  - Best to bring links directly to the right chip
  - If not, at least to the same module
  - Or from a module in the same crate (fast parallel transfer)
  - Avoid need for high latency serial transfers
    - Either between modules in the same crate or different crates
L1 constraints affect the layout of RODs and FE links

---
Channel and Link Organisation (2)
Little guidance yet from simulation
  - Assume the worst cases (from FE and ROD viewpoint) and look at the implications
Assume L1 primitives formed from all depth samplings
  - For EM and hadronic layers separately (at this point)
    - Sending separate depth samplings to L1 is easier for organising links
Assume L1 primitives must cross calo boundaries
  - Process Barrel/Endcap cells together in same chip
  - Assume crack scintillators for EMB/EMEC boundary
    - Implies LAr and Tile RODs sharing crates
Worst possibility? Full EM+hadronic depth summing
  - Inevitable latency penalty, high degree of convergence between EM and hadronic RODs (and shared crates)

---
Present Mapping Stages
Many stages
Lots of patch panels
  - Humble TCPP is ~2Gbit/s remapping device with ~0 latency and power!
Easy areas regularised in one step at receivers
Tricky areas needed many successive steps
Never really managed it with the FCAL

---
Possible Upgrade Mapping Stages?
Fewer steps available?
  - Unless we add latency with an additional reorganisation
Start with FE boards
  - May need several different channel to link mappings?
Remap FE to ROD links
  - Signals in depth and across boundaries to same place
Minimal (low latency) transfers in ROD crates?
Regroup (and duplicate) ROD to L1Calo links

---
ATCA-based ROD Crate?
New crate: new architecture for control/configuration?
No crate CPU or control bus
Separate network and TTC++ connection to each ROD
Flexible and scalable set of PCs to configure N RODs/PC
Different TTC partitions can (but need not) share crates
Can run separate standalone partitions for calibration
Many configurations possible

---
ROD Issues (1)
Two TTC partitions in one ROD at boundaries
Tile baseline (DAQPP) has all four partitions:
  - Q1 (curiosity): how to run partitions independently?
  - Q2 (request!): can LAr do the same?

---
ROD Issues (2)
Granularity of FPGAs:
  - Probably want little or no transfer between chips?
  - If so, N links input to one chip define the eta,phi space of n links output to L1
  - Can all depth layers be really brought together?
    - Depends on cells/link, links/chip, chips/ROD
Eta,phi space covered by whole RODs:
  - Any need to transfer data between RODs requires congruent eta,phi spaces covered by those RODs
    - Eg for Tile RODs to send crack scintillators to EMB/EMEC RODs
Sparseness at higher eta
  - Changing ratio of input cells per “tower” with eta
  - Underutilised RODs or reconfiguration of input:output links