Title
L1Calo Upgrade Phase 2
Murrough Landon
11 January 2010
- Introduction and timescales
- Granularity and algorithms
- RODs, links and mappings
- L1Calo design?
- Summary

---
Introduction
- LHC phase 2 luminosity upgrade expected ~2020?
  - Aiming to reach about 10^35, but no increase in energy
- Trigger requirements
  - Still interested in the same objects (W,Z,etc)
  - Hope to keep thresholds as close to 10^34 menu as possible
  - But the interaction rate and pileup is much higher
  - So we will need a significantly more discriminating trigger
    - Over 99% of “phase 0” L1Calo electron triggers are jets
  - Use much finer granularity information from the calorimeters
- Towards phase 2
  - LAr and Tile are already doing design and prototyping work for new front end electronics and new RODs
  - L1Calo needs at least to start design and simulation studies

---
Timescales
- Earliest date for phase 2 is (currently) about 2020
  - Install and commission new trigger in 2019?
  - Production and testing in 2018?
  - Final prototypes and preproduction in 2017?
  - Final(?) design and technology choices in 2016?
- We need to have a very good idea of what we want to do in about five years from now
  - Which needs plenty of simulation studies
  - Experience and testing of links, FPGAs, ATCA crates, etc
    - (ATCA = Advanced Telecomms Computing Architecture)
    - The GOLD module from Uli could be a good test bed
  - Design discussions with calorimeter communities
    - Small working group has just started...

---
Likely Phase2 Trigger
- Fast Level0 Calo and Muon RoIs
  - For L1 track trigger(s)
- Slower Level1 topological trigger
  - Using a combination of calo, muon, inner tracker (and MDTs?)
  - May also have L1Calo refinement of original L0Calo trigger?

---
Calo Front End, ROD and L0Calo Links
- Digitise all cells every BC and transmit to RODs in USA15
- Preprocess for L1Calo
  - Et (or energy?) per BC
  - Maybe also precise timing?
  - Fine granularity sums
  - Location within mini towers?
    - Coordinate of EM strip max?
  - Quality flags
    - Pile up detected
    - Fine structure in EM strips?
      - Eg for π0 rejection

---
Possible Additional L1Calo Stage?
- Suggestion to use the L1 stage also for refining the L0Calo decision
  - Only useful for EM layer?
- Adds complexity to the calorimeter RODs as well as the L1Calo trigger
- Need a good idea of how it would be used
  - Simulation study?!

---
Granularity
- Present L1Calo
  - Mainly based on 0.1*0.1 towers in both EM and hadronic
  - This is the hadronic layer detector granularity
  - But EM layer has much finer granularity – unused so far
- L1Calo Phase 2
  - Not much change in hadronic layer?
    - Would more depth samplings be useful?
    - Might anyway be worth separating Tile D cells (0.2*0.1 geometry)
  - Expect big (tenfold?) increase in EM data to phase 2 L1Calo
    - Need to study what is the most useful information to send
    - Plenty of opportunities for people to work on simulation!

---
EM Barrel Geometry
- Each layer has a different geometry
  - Uniform in eta, except for barrel/endcap transition region

---
EM Endcap Geometries
- Seven different layouts between eta=1.4 and eta=3.2
- Many different ways cells are grouped in front end boards
- Also other layouts in the hadronic layer and FCAL

---
Algorithms
- Basic sliding window with finer granularity
- Try to import good algorithms from present L2
- Best EM selection is based on shower shape:
  - Look at ratio of 3*7 vs 7*7 middle layer cells
  - Simulation question: how does this degrade with granularity
    - Suppose we had sums of 2 middle cells (matching back layer cell)
    - Would have to look at 4*7 vs 8*7 cells
- Next best (for π0 rejection):
  - Look for fine structure (double peaks) in strip layer
  - This really needs the full granularity to be useful
    - Probably too much data to ship to L0Calo (could go to L1Calo?)
    - Good candidate for more sophisticated ROD preprocessing?
  - Simulation/algorithm/firmware question: what would be the best way to process and transmit this information?

---
Links to L0/L1Calo (1)
- EM layer:
  - Suggest one 10 Gb/s fibre per 0.1*0.1 tower (all layers)
    - Allows about 200 bits of payload data per BC (would like more!)
  - Example allocation of bits (all depth samplings separate)
    - Keep phi granularity (middle/back), sum to 0.05 in eta
    - Eight 10 bit (Et+quality?) back layer values [80]
    - Eight 10 bit middle layer sums plus max cell bit [88]
    - Two 10 bit strip layer sums plus 8 coordinate/quality bits [36]
    - Two 10 bit PS layer sums plus 1 coordinate bit [22]
    - Total 226 bits (and we would like some spare bits too)
  - Maybe additional 1 fibre with low granularity (0.1*0.1) sums
    - Useful if jet/energy trigger is in a separate FPGA or module
  - Additional fibres per 0.4*0.2 with extra info for L1 stage?
    - Full strip layer information for π0 rejection and track matching?
    - Precise timing for z vertex and/or slow heavy exotic particles?

---
Links to L0/L1Calo (2)
- Hadronic layer:
  - Suggest one 10 Gb/s fibre per eight 0.1*0.1 towers
  - Allows about 25 bits per tower
  - Good to (slightly) underuse the bandwidth
    - Need to cope with extra cells in overlap regions
    - Eg crack and gap scintillators
    - Tile and HEC cells in 1.4 to 1.6 region
    - Might have up to ten towers per link in places
- More compact in low granularity endcaps/FCAL?

---
LAr and Tile RODs
- LAr
  - Latest aim is for one ROD to cover one half FE crate
    - Or same number (1800) of cells with different eta*phi shape
    - ROD would contains four TCA mezzanines (with 1 FPGA?)
  - L1Calo (my!) preference
    - One EM ROD mezzanine covers a “domino” of 0.4*0.2 (eta*phi)
      - Larger area in the low granularity EM endcap region, HEC and FCAL
    - Aim to keep the shape the same across the eta phi space
      - Easier for fanout – but harder in standard EM Endcap region
- Tile
  - Current Tile proposal: ROD covers 3.0*0.1 in eta*phi
    - Much less dense than LAr ROD: could be more ambitious!?
  - L1Calo (my!) preference:
    - ROD covers 0.2 in phi (either split at eta=0 or more dense)
    - Match the EM 0.4*0.2 domino when grouping towers on links

---
LAr EM Barrel/Overlap Mapping
- Attempt to map links from front end boards (FEBs)
  - Tricky regions need duplication/quadruplication of fibres

---
ROD Outputs to L0/L1Calo?
- EM layer
  - Probably four 10 Gb/s SNAP12 bundles per ROD
    - One per mezzanine (less if higher speed links which is likely)
    - Same for all eta, but RODs & links somewhat underused at high eta?
- Hadronic layer (HEC and Tile)
  - Depends on density of channels per ROD
  - LAr HEC/FCAL RODs likely to be as dense as EM RODs
  - For present Tile ROD, probably one SNAP12 bundle per ROD
    - Could have two or four as for EM RODs with higher density RODs

---
Inputs to L0/L1Calo
- One 0.4*0.2 area in eta*phi might have:
  - 8 EM fibres covering one 0.1*0.1 tower each
  - 1 Hadronic fibre covering eight 0.1*0.1 towers
  - Perhaps additional 1 EM fibre with low granularity sums
    - Useful if Jet/Energy algorithms are in a separate FPGA
  - And maybe additional fibres per 0.4*0.2 area with extra information used only by L1 trigger (not for L0)
- Regroup to one SNAP12 with EM+Had fibres
- Optically duplicate each bundle at the same time
  - Intercrate fanout

---
L0Calo Phase 2 Architecture? (1)
- Single processor module (0.8*0.8)
  - For all objects: EM, tau, jet
  - Maybe 4 TCA mezzanines like LAr ROD?
  - If so, could have one FPGA per 0.8*0.2
    - If we have one fibre per 0.1*0.1 tower:
    - 11*5 EM fibres plus 4*3 hadronic fibres
    - Separate FPGA (one per module) for jets?
      - Unless one 2015 FPGA handles lots more inputs?
    - Total of 88 0.1*0.1 fibres plus 2*28 0.4*0.2 sum fibres per module
    - Around 12 SNAP12 fibre bundles
    - About 1.5 Tbit/s total bandwidth per module
- Or could imagine separate JEM
  - One per octant crate covering all eta
    - Same module, different firmware?

---
L0Calo Phase 2 Architecture? (2)
- Phi octant layout
  - Intercrate fanout from RODs, eta fanout via backplane
  - Output to global topological merger
  - ROD/ROS in same crates?

---
Summary
- Trying to get a rough L0/L1Calo design
  - Are our current thoughts reasonable?
- L1Calo/LAr/Tile working group starting discussions
  - Organisation of RODs and links, bandwidth, etc
  - Granularity of L0/L1 sums and content of data
  - Any other preprocessing we would like
- Prototyping and technology demonstrators under way
  - Especially in LAr and Tile
- Important to get input from simulation!