Title
L1Calo Upgrade Phase 2
Murrough Landon
2 February 2010
- Phase 2 Functional Blocks?
  - Thoughts on L1 “refinement” of L0
- Simulation framework
- Phase 1 Online SW

---
“L1Calo” Functional Block Diagram?

---
“L1Calo” Functional Block Summary
- L0Calo
    - Big system (64 modules, 8 crates?), ~40Tbit/s
- L0Topo/Merger
    - One or few modules(?), ~2Tbit/s
      - May be fairly simple: do we need much more than merging for L0 RoIs?
- L1Calo
    - One full crate system?, ~2Tbit/s, very complex FW
      - Limited rate reduction (π0 rejection), may not be needed? Or phase 2.5?
- L1Topo
    - One or few modules(?), few Gbit/s
- ROD
    - Scattered system (1 module per crate?)
      - HW/FW/SW experts willing & able to travel to all test rigs!

---
Functional Blocks: Separate or Combine?
- L0xxx and L1xxx
  - Running at different rates (40 MHz vs 500 kHz)
  - Easier to keep separate?
- Except L0CTP & L1CTP?
  - Combine to provide RODs & FEs with single L0/L1 interface?
  - But then single CTP needs sets of L0 and L1 trigger inputs
- *Topo and *CTP?
  - CTP has detector interface and inputs from other triggers
    - Luminosity, forward, calibration triggers, etc
  - Keep CTP separate from topological triggers?
    - But *Topo would probably take over MuCTPI function?
    - Unless separate MuCTPI makes it easier for L1Calo group to provide the L*Topo systems?

---
L1Calo (phase 2) Functional Block (1)
- No need for L0 RoIs?
  - Must have fibre(s) from each ROD/mezzanine anyway
    - Some RODs (FCAL?) may be hot: send data every L0A
  - Plenty of latency available: simplest to send everything?
    - Strips are 50% of the data, so everything is only factor 2 more
  - Rerun all algorithms at L0A rate, now with full granularity
- Input Data Volume
  - All calo cells preprocessed to give Et, time, quality flags
    - Say 20 bits/cell, 200k cells => 4 Mbit data (compressible?)
    - On LAr RODs, ~500 cells/mezzanine => 10 kbit per 0.4*0.2 eta*phi
    - Transmit in about 0.5µs over one 20 Gbit/s fibre
    - Tile: one such fibre per ROD is more than enough
  - Average L0A rate 500 kHz (ie 1 per 2µs)
    - Need some derandomising, limits on instantaneous L0A rate
    - Even with 2µs transmission latency, still several µs left for logic

---
L1Calo (phase 2) Functional Block (2)
- Total L1Calo Input and Output
  - Total ~512 * 1 fibre per mezzanine => 512 20 Gbit/s fibres
    - EM 432 mezzanines, LarHad 32 mezzanines, Tile ~64
    - Output: 8 fibres, one per 0.8*0.8 RoI map (as L0Calo)?
- Example Architecture
  - Single crate, eight modules
  - 64 * 20 Gbit/s fibres/module
  - Module covers 0.8 in eta and all phi
    - 100% fanout to neighbours

---
Phase 2 Simulation Framework
- Need new simulation toolkit for phase 2
  - New summing of cells to minitowers
  - New algorithms run on these minitowers
  - Would like several variants of them
  - Volunteers?

---
Phase 1 Module Services SW
- How to communicate with modules?
  - Existing: SW layer over VME driver to FW register model
- Proposed phase 1 TCM: ethernet to all modules
  - Keep vaguely similar SW model?
    - ATCA modules stay fairly dumb (as seen by SW!)
    - New protocols for SW to address registers/memories
    - SW running elsewhere loads data into modules
  - Or ATCA modules get smarter?
    - Use CPU cores in FPGA
    - SW runs in the module
      - Still need some model to interact with FW
    - Module fetches its data from external sources
  - Any idea how other ATLAS groups are thinking?