Title
ATLAS L1Calo Phase2 Upgrade
Murrough Landon
(on behalf of ATLAS/TDAQ/L1Calo)
11 March 2011
- Phase 2 Overview: L0 and L1
- Possible L0/L1Calo architecture
  - Links, algorithms, hardware, R&D

---
Scenarios for Level-1 in Phase 2
- ATLAS constraints
  - Hard to access some muon chambers even in a long shutdown
    - Some front end electronics may be impossible to replace
    - May have to live with maximum latency of 3.2µs
- Low latency scenario
  - Level-1 upgrade limited to 3.2µs
  - Not enough for level-1 track trigger
- Two stage L0/L1 scenario (preferred)
  - Level-0 stage for calo/muon triggers within 3.2µs
    - Send regions of interest to seed readout of regional track trigger
    - Ideally run at up to 500 kHz (though legacy systems may limit this)
  - Second stage level-1 trigger including calo/muon/track
    - Asynchronous, latency up to 9.6µs or possibly much longer

---
Overview of Phase 2 (L0/L1 scenario)
Talk by
Robert
Richter
Talk by
Matt
Warren

---
L1Calo Changes for Phase 2
- Existing L1Calo system
  - Separate trigger & readout paths
  - 7k analogue trigger towers per BC
  - Analogue gain calibration per tower
  - Digital BCID filter per trigger tower
  - Digital trigger algorithms
- Phase 2 proposal
  - Digitise all calo cells every BC: 160 Tbits/s
  - Single readout+trigger path off detector
  - Single calibration & BCID filter per cell
  - Trigger sums formed off detector
  - Fine granularity trigger algorithms

---
Baseline Phase 2 L1Calo Architecture
In the low latency scenario, only the L0 blocks are possible

---
Phase 2 L1Calo Components
- L0Calo:
  - Find EM, Tau, Jet objects and Et sums every BC
- L0Topo:
  - Topological processor: merge L0Calo & L0Muon results
- L1Calo:
  - Asynchronous refinement of L0Calo using full calo data
    - Likely to be driven by L0 RoIs
- L1Topo:
  - Final topological processor for L1Calo, L1Muon & L1Track
- L0 & L1 CTP:
  - Final trigger decisions, interface with detectors
    - Interface with topological processors to be defined

---
Calo ROD – L0Calo Interface
- Calo Readout Driver (ROD) functions for L0Calo:
  - Derive calibrated Et from digitised pulses
    - No issues with analogue saturation
  - Assign Et to correct bunch crossing
  - Provide quality flags from optimal filter (pile up, etc)
  - Form sums of calorimeters cells into “mini towers”
    - Definition of mini towers (or “L0 primitives”) to be defined
    - EM layer: both fine and coarse sums (for EM & Jet triggers)
  - Possibly run algorithms on cells within one ROD FPGA
    - Eg pi0 rejection using LAr EM strips
  - Transmit mini towers to L0Calo
  - Pipeline full data (for every cell) for use by L1 stage (& DAQ)

---
Calo ROD – L0Calo Links
- Baseline: 10 Gb/s links => 200 bits per bunch crossing
- Hadronic layer (and coarse EM sums for jet trigger):
  - One 10 Gb/s fibre link per 0.4*0.2 (or 0.2*0.4) in eta*phi
    - Can have finer eta*phi and depth granularity than now for jets
- EM layer fine granularity for EM/Tau algorithms:
  - One 10 Gb/s fibre link per 0.1*0.1 tower
    - 200 bits: more detail on eta, phi and depth
    - Concentrate bandwidth on middle layer?
      - Contains most of the energy
      - Heavily sum the strips layer

---
Phase 2 L0Calo Algorithms
- Sliding windows, now with finer granularity
  - Limitations will be fanout and number of inputs per FPGA
    - Expect O(50) 10 Gb/s links into Virtex 7
- Adopt L2 EM/Tau ideas
  - L2 “R core”: ratio of 3*7 to 7*7 LAr middle layer cells
    - L0Calo bandwidth might require middle layer cells summed in pairs
- Investigating benefits of larger jet environment...
  - Present 0.8*0.8 eta*phi jets use 0.4*0.4 RoI maximum
    - Better to know if 0.8*0.8 area is a maximum within its environment
    - Problem: much larger fanout and more fibres per FPGA
    - Larger environment with 0.1 granularity may need separate jet system
    - Needs some simulation work...

---
Possible L0Calo Implementation
- “Strawman” module
  - Covers 0.4*1.6 eta*phi
  - Both EM/Tau and Jet
    - Resolve overlaps locally
  - Fully custom backplane
    - Fanout to adjacent slots
    - Passive optical fanout for adjacent crates in phi
  - Four full ATCA crates
    - ETSI 16 slot 23” crates?

---
Level-1 Calo Processor
- Refinement of level-0 calo possible at the level-1 stage
  - Can be seeded by level-0 regions of interest
  - Gets full granularity calorimeter data for L0 events
- Long latency and asynchronous processing
  - Can consider using CPUs or graphics processors
  - Could use event based multiplexing (CMS style)
  - Variable processing time per event (similar to present L2)
  - But need to output events in the correct order
    - This is probably a detector requirement
    - It may also be required between each L1 functional block

---
Topological Processors: L0 and L1
- Level-0 topological processor
  - Evolution of phase 1 topological processor: see phase 1 talk
  - Similar set of algorithms as phase 1
    - But benefitting from greater precision in eta, phi and Et
    - Scope for additional algorithms...
- Level-1 topological processor
  - Combine calo, muon and track objects found at L1
    - Track/shower matching, combined muon tracks
  - Long latency and asynchronous processing: could use CPUs?
  - Design to use either L0 or L1 calo and muon inputs?

---
R&D Work
- Already designing ATCA demonstrators for phase 1
- More demonstrators being planned
  - Study PCB simulation: really understand high speed links
  - Optical fanout and patching
- Medium term: build up “slice” of full phase 2 system
Calo
ROD
full granularity calo data
L0 Muon
mini
towers
L0 Calo FEX
L0 Topo (global)
L0 CTP
L1Calo FEX
L1 Topo (global)
L1 CTP
L0A
ROD
ROD
ROD
ROD

---
Summary
- “Straw man” design emerging - at least for L0, but...
  - Needs more work on the details and input from simulation
  - Need to define algorithms
  - Need to estimate latency of L0Calo+L0Topo
- Evolutionary approach
  - Use phase 1 topo processor as L0Topo prototype
- Started thinking about asynchronous L1 stage
- ATLAS L1 Technical Proposal now being written
- R&D program emerging for phase 2
  - Technical demonstrators followed by prototype “slice”
  - LAr & Tile planning phase 2 prototypes to be used in ATLAS
    - Hope to feed outputs from these into L0Calo prototypes...