Title
Phase2 Level-0 Calo Trigger
Murrough Landon
27 June 2011
- Phase 2 Overview: L0 and L1
- L0Calo Functionality
- Interfaces to calo RODs
- Interfaces to L0Topo

---
Baseline Phase 2 L1Calo Architecture

---
L0Calo Functionality
- Real time algorithms:
  - Find EM clusters, Tau/hadrons
    - Use fine granularity as much as possible to discriminate against QCD
  - Find jets
    - Ideally on the same module, but separate jet system is an option
    - Possibly larger size than at present, eg 1.2*1.2 in eta*phi?
  - Sum E, Et and missing Et components per L0Calo module
- Transmit results
  - EM/Tau/Jet RoIs and energy sums in real time to L0Topo
    - On L0A also send them to L1Track and L1Calo
- Readout
  - Buffer results for eventual L1A
    - Also send L0 readout to RODs for monitoring at L0?

---
L0Calo Algorithms
- Sliding windows, now with finer granularity
  - Limitations will be fanout and number of inputs per FPGA
    - Expect O(50) 10 Gb/s links into Virtex 7
- Adopt L2 EM/Tau ideas
  - L2 “R core”: ratio of 3*7 to 7*7 LAr middle layer cells
    - L0Calo bandwidth might require middle layer cells summed in pairs
    - NB initial simulation results are disappointing for calo only trigger
- Investigating benefits of larger jet environment...
  - Present 0.8*0.8 eta*phi jets use 0.4*0.4 RoI maximum
    - Better to know if 0.8*0.8 area is a maximum within its environment
    - Problem: much larger fanout and more fibres per FPGA
    - Larger environment with 0.1 granularity may need separate jet system
    - Needs some simulation work...

---
L0Calo Components (1)
- Optical fanout and patch network
  - Fibres from calo RODs need to be duplicated/reorganised
    - Fanout across crate boundaries
    - Regroup fibres for optimum layout of L0Calo modules?
      - Merge EM and hadronic fibres in same eta*phi area to minimise crossing tracks
    - Separate L0 and L1 fibres from the same ROD
    - May need active components if passive fanout is not good enough
  - Significant component which needs some R&D work

---
L0Calo Components (2)
- Rear transition modules
  - Optical receivers and fanout to adjacent L0Calo modules
    - Possible alternative: more optical and less electrical fanout
- Custom ATCA backplane
  - Transmission from RTMs to modules in same/next slots

---
L0Calo Components (3)
- L0Calo module (Sam)
  - Cover 0.4*1.6 eta*phi
    - Unless 0.8*0.8 shape better for fat jets?
  - Inputs via backplane
  - Find EM/Tau and Jet on same module
    - In separate FPGAs
    - Jet FPGAs resolve EM/Tau overlaps
    - Transmit combined RoIs to L0Topo
  - Four full ATCA crates
    - Or 8 for 0.8*0.8 option?

---
L0Calo Components (4)
- Auxiliary modules
  - Clock/trigger distribution (“TCM”)
    - But may not be room for a dedicated module per crate
    - Distribute GBT signals directly to each module?
- Readout
  - L0 ROD to gather data for L0 accepted events
  - Local L0 event building to monitor trigger performance at L0?
  - Buffer data for readout to DAQ on L1A

---
L0Calo System
- Four full ATCA crates (14 or maybe 16 slots)
  - Each crate processes one quadrant in phi
  - Alternative with 0.8*0.8 modules uses 8 partly full crates
- Two (or four) racks
  - Plus same again for fibre empire?

---
Calo ROD – L0Calo Interface
- Calo Readout Driver (ROD) functions for L0Calo:
  - Derive calibrated Et from digitised pulses
    - No issues with analogue saturation
  - Assign Et to correct bunch crossing
  - Provide quality flags from optimal filter (pile up, etc)
  - Form sums of calorimeters cells into “mini towers”
    - Definition of mini towers (or “L0 primitives”) to be defined
    - EM layer: both fine and coarse sums (for EM/Tau & Jet triggers)
  - Possibly run algorithms on cells within one ROD FPGA
    - Eg pi0 rejection using LAr EM strips
  - Transmit mini towers to L0Calo
  - Pipeline full data (for every cell) for use by L1 stage (& DAQ)

---
Calo ROD – L0Calo Links
- Baseline: 10 Gb/s links => 200 bits per bunch crossing
  - Assumes 25ns bunch crossings: half for 50ns LHC?
- Hadronic layer (and coarse EM sums for jet trigger):
  - One 10 Gb/s fibre link per 0.4*0.2 (or 0.2*0.4) in eta*phi
    - Can have finer eta*phi and depth granularity than now for jets
- EM layer fine granularity for EM/Tau algorithms:
  - One 10 Gb/s fibre link per 0.1*0.1 tower
    - 200 bits: more detail on eta, phi and depth
    - Concentrate bandwidth on middle layer?
      - Contains most of the energy
      - Heavily sum the strips layer
- Links to L1Calo
  - Originally said 1 fibre per 0.4*0.2 (LAr): but may need more!

---
L0Calo Inputs to L0Topo
- One (or two) fibre(s) per L0Calo module
  - 200 (or 400) bits per 25ns bunch crossing
  - Perhaps 60-80 bits for Et, Ex, Ey, E
  - Leaves 120 (or 320) bits for RoI objects in 0.4*1.6 area
  - 25 bits per object => ~five (or twelve) RoIs per L0Calo module
    - Five RoIs may be a bit tight, twelve seems luxurious
    - 64 (or 128) inputs per L0Topo FPGA might be OK (or is too much)
- Suggestion: separate objects from sums
  - One (underused) fibre for Et, Ex, Ey, E
    - Processed in dedicated L0Topo FPGA
  - Second fibre for about eight EM/Tau/Jet RoIs

---
L0Topo Implementation & Algorithms
- Implementation much like phase 1 proposals?
  - Few modules in (part of) one ATCA crate
  - All (or most) fibres duplicated to each module
    - But different modules may run different sets of algorithms
    - All energy sum fibres to one module? Results via backplane
    - 64 L0Calo RoI fibres plus muon fibres may be too much for one FPGA
- Algorithms
  - Also similar to phase 1
    - Benefitting from greater precision in eta, phi and Et
    - Though EM/Tau overlaps with Jets hopefully removed at L0Calo
    - Scope for additional algorithms...
      - Possible benefit in having total E for use in missing Et algorithms?

---
R&D Work
- Already designing ATCA demonstrators for phase 1
- More demonstrators being planned
  - Study PCB simulation: really understand high speed links
  - Tests needed for optical fanout and patching
- Medium term: build up “slice” of full phase 2 system
Calo
ROD
full granularity calo data
L0 Muon
mini
towers
L0 Calo FEX
L0 Topo (global)
L0 CTP
L1Calo FEX
L1 Topo (global)
L1 CTP
L0A
ROD
ROD
ROD
ROD

---
Points of Attention
- Calo ROD – L0Calo links: bandwidth and organisation
  - Changes have major impact on ROD and L0Calo organisation
  - Status of LAr LOCs6?
  - Impact of increasing eta*phi space of “jet” fibres
  - What if (when?) LHC irrevocably decides for 50ns bunches
  - Need to recheck required bandwidth to L1Calo
- Usefulness (or not) of fine granularity
  - More simulation and/or new algorithm ideas
    - Keep high granularity L0Calo as preferred option in case of surprises
- Implications of larger jets
- R&D programme, timescale, division of labour...